## Slide 1: XCCDF Evaluation Reference Architecture
AN Operational Model for COMBINING automated and manual check Results
David E. Ries
An open-source SCAP library for Java™, with plug-ins for remote and offline scanning.
™
Notes: jOVAL is a project of Farnam Hall Ventures where David Ries is a partner.

## Slide 2: Agenda
Background & Goals
XCCDF Concepts
Lessons from XCCDF-exec
Lessons from gOCIL.org
OCIL vs. Automated Check Systems
Enterprise Workflow Management
Proposed Reference Architecture
Implications on XCCDF Contract
Specification Impact
Additional Open Questions
Q&A

## Slide 3: Background
Farnam Hall Ventures
  XPERT: XCCDF interpreter (OVAL, SCE, OCIL)
  jOVAL: OVAL interpreter
  gOCIL: OCIL interpreter
We want to support “continuous” assessment of devices.
Adding OCIL into the equation posed challenges
  How to route Questionnaires?
  Do we have to wait for OCIL results to produce an XCCDF result?
  If we decide to assess machines more frequently than humans, are composed XCCDF results valid?

## Slide 4: Goals
Share a reference architecture for evaluating XCCDF checks containing both automated and manual checks
  Feedback: is this a useful, generally applicable approach?
  Does this approach inform the XCCDF use case(s)?
Discuss specific challenges we faced and offer potential solutions
  Do we agree on the issues?
  Should they be addressed in XCCDF (vs. tooling or other standards)?

## Slide 5: XCCDF Concepts
XCCDF encodes a security policy for a class of devices comprising a collection of security configuration rules
Rules can refer to external check systems
  OVAL: fully automated checks collect data from device
  OCIL: partially automated checks collect data from person
  SCE: fully automated checks collect data from device
  Other: proprietary and future check systems
Although XCCDF doesn’t prescribe a processing model, we tend to think of it as fully automated, executable job
  Run automated checks and generate a result that represents a system’s conformance to the Benchmark at a moment in time

## Slide 6: Lessons from XCCDF-exec
XCCDF-Exec: reference implementation
Processing flow: one device, synchronous
  OVAL checks: runs OVALDI on local machine to generate OVAL result
  OCIL checks: runs OCILQI to display Questionnaire to current operator
  Generates one XCCDF result
Implications
  The device running the content is the subject of all Questionnaires*
  All questionnaires can be answered by the same person*
  An XCCDF result represents results for all checks, run once during a narrow time window
* Discussed during OCIL 2.1 proposal discussion, Developer Days 2012 by Jim Ronayne

## Slide 7: Lessons from gOCIL.org
gOCIL: enterprise-ready OCIL interpreter
  Introduced at developer days last year
  Enables secure, distributed, discontinuous, tablet/phone-ready OCIL collection
  Demonstrates possibility of automated collection of manual checks without real-time dependency
Positive feedback, minimal adoption
  Very early on the OCIL adoption curve (minimal content, usage)
  Open questions around collection alongside automated checks
    Orchestration, routing, timing, architecture

## Slide 8: OCIL vs. Automated Check Systems
Differences between devices and people
  Availability, response times, repeated queries
  We typically know a device’s role in it’s own security, but may not know how to map from an org chart to a device’s security roles
Challenges
  Routing: map from content/device to Questionnaire respondent
  Communications: securely communicate with respondent
  Workflow: implement workflows to handle typical situations
    Follow-up and escalation if Questionnaire is not completed in a timely fashion
    Compensation for changes in role (respondent is fired, promoted, on vacation)
    Selection amongst multiple acceptable respondents
    Etc.

## Slide 9: Enterprise Workflow Management
Ticketing System
Asset Management
Helpdesk
SLAs/Contracts
Email
ITSM
  Workflow management solutions already entrenched in the enterprise
  Enterprise ticketing systems are the pre-existing backbone in mature process-oriented organizations, such as those that are commonly subject to regulatory compliance requirements.

## Slide 10: Don’t Re-Invent the Wheel
Ticketing systems are designed to:
  Manage the collection of information from humans
  Integrate with LDAP and email systems for authentication and notification
  Manage customizable processes, to include:
    Response times
    Escalations and alternate execution paths
  Integrate with asset management and change control systems
    These commonly contain information about who is responsible for particular IT assets
Natural integration hubs for IT
Asset Management
Helpdesk
SLAs/Contracts
Email
ITSM

## Slide 11: SACM Architecture: Basic Grouped Entities*
Evaluator
Data Collector
Collector/Processor
* Contributed to SACM by Gunnar Engelbach
Results Viewer
Results Datastore
Controller
Controller Front-End
Management System
Notes: This is Gunnar’s slide from the SACM mailing list. This made a ton of sense for us, probably because this is what our product looks like too. These are logical components grouped by likely physical components.

## Slide 12: Proposed Extensions for OCIL
Evaluator
Data Collector
Processor
Ticketing System
Survey Collector
Collector
Results Viewer
Results Datastore
Controller
Controller Front-End
Management System
Notes: We extended this architecture, adding a ticketing collector, separating processing and collection into two logical tiers. The analog of evaluator for OCIL is ticketing system, because once controller has dispatched job, Ticketing system is managing process.

## Slide 13: Process Flow for Asynchronous Collection
Evaluator
Data Collector
Ticketing System
Survey Collector
Results Datastore
Controller
1
2
3
4
Controller separates request by system
  Automated checks dispatched to the evaluator
  Manual checks dispatched to a ticketing system
Ticketing system…
  Creates survey in the survey collector
  Polls the collector and obtains result
  Manages notifications, timeouts, escalations, etc.
Controller obtains/stores system results as they become available from the collectors
When all collection is complete, controller dispatches them to the evaluator for combination

## Slide 14: Implications on XCCDF Contract
If we accept ticketing as model for addressing concerns external to XCCDF, does that help crystallize what’s required of XCCDF to support enterprise-specific workflows?
Questionnaire Routing
  XCCDF would need to provide metadata sufficient to enable a ticketing business rules engine to create and assign a Questionnaire completion task
Remediation
  XCCDF would need to provide metadata sufficient to enable a ticketing business rules engine to create and assign a change control task

## Slide 15: Specification Impact: Routing
Needed: a taxonomy sufficient to enable ticketing system to map from content and device to respondent
  Device and Context: platform (AI), location, service context, CIA
  Content and/or Role
NIST IR7692: OCIL 2.1 Draft 1, appendix B.4
  <Rule id="xccdf_com.ex_rule_Rule1" selected="false">
  <title>Unused DBMS components should not be installed.</title>
  <metadata>
  <ocil_routing:target_respondent_role
  xmlns:ocil_routing=”http://iase.disa.mil/roles”>
  DBA
  </ocil_routing:target_respondent_role>
  </metadata>
  <check system="http://scap.nist.gov/schema/ocil/2">
  <check-content-ref href=“..." name=“..."/>
  </check>
  </Rule>

## Slide 16: Specification Impact: Check Aging
Needed? explicit max age at check level to help define the meaning of XCCDF result
  OCIL/OVAL results have @start_time and @end_time
  XCCDF results have @start-time and @end-time
  Max-age: maximum time difference between XCCDF@start-time and check@end_time in seconds
  <Rule id="xccdf_com.ex_rule_Rule1" selected="false">
  <check system="http://scap.nist.gov/schema/ocil/2" max-age=“360”>
  <check-content-ref href=“USGCB-Windows-7-OCIL.xml" name=“..."/>
  </check>
  </Rule>
  <Rule id="xccdf_com.ex_rule_Rule2" selected="false">
  <check system="http://oval.mitre.org/XMLSchema/oval-definitions-5"
  max-age=“7884000”>
  <check-content-ref href=“USGCB-Windows-7-oval.xml" name=“..."/>
  </check>
  </Rule>

## Slide 17: Additional Open Questions
One OCIL result for multiple devices/XCCDF results?
  A respondent completes OCIL Questionnaire once for all machines under her purview.
Multiple OCIL results for one check (multiple respondents)?
  XCCDF Specification, 7.2.3.5.2 Rules with Multiple Results
    …For example, a host OS benchmark could contain <xccdf:Rule> elements that apply to all users, and a router benchmark could contain <xccdf:Rule> elements that apply to all network interfaces.
    ...A processing engine that performs a checking system test MAY deliver one or more results in response to a check...
Others?

## Slide 18: Questions
Q&A

## Slide 19: Example Application Architecture